Automated Irrigation System

Goal: indoor / garden plants automatization.

Tasks:
1. Measure soil moisture
2. Measure temperature
3. Measure light
4. Drive Irrigation pump
5. log data

Plan:
- Moisture: 555 timer RC capacity measure
- Temperature: in box measurement
- Light: in box measurement
- Watering pump: common source motor drive circuit

Controller: EFM32GG Giant Gecko Starter Kit
IDE: Simplicity Studio 5 IDE
PCB editor: KiCAD

The microcontroller drives the sensorts, and reads temperature, moisture and light data. Based on measured data, the controller drives an external pump, to irrigate the plants soil.

Temperature sensor:

The used IC for temperature measurement is an LM75C. The chip uses I2C bus to communicate with the controller.

Moisture sensor:

Moisture measuring method is based on capacity measurement. The measurement is based on a TLC555 timer IC in astable mode.

Light sensor:

Light measurement is done via VEML7700 IC.

Package:

Project is packaged in an IP67 plastic case.

-Pump:

The control element of the system is one 12V pump, a Barwig 0333.

-Power Supply:

The device is powered with an LPV-35-12 power supply unit, which provides 12V DC for the pump.
Alternatively a barrel jack input is supported if 12V DC input is available. When the barrel jack is in use, LPV power supply is out of use.

-Connectors:

The board has five connectors.
1. Pin array to connect to the giant gecko controller. (2x10 pin array female)
2. screw terminal for capacity measure device
3. screw terminal for pump drive
4. screw terminal for 12V DC input
5. barrel jack, for 12V DC input

-Schematic:

-PCB layout:

-Prototype Hardware: