Automated Irrigation System

Goal: indoor / garden plants automatization.

Tasks:
1. Measure soil moisture
2. Measure temperature
3. Measure light
4. Drive Irrigation pump
5. log data

Plan:
- Moisture: 555 timer RC capacitance measure
- Temperature: in box measurement
- Light: in box measurement
- Watering pump: common source motor drive circuit

Controller: EFM32GG Giant Gecko Starter Kit
IDE: Simplicity Studio 5 IDE
PCB editor: KiCAD

The microcontroller drives the sensorts, and reads temperature, moisture and light data. Based on measured data, the controller drives an external pump, to irrigate the plants soil.

Temperature sensor:

The used IC for temperature measurement is an LM75C. The chip uses I2C bus to communicate with the controller.

Moisture sensor:

Moisture measuring method is based on capacitance measurement. The measurement is based on a TLC555 timer IC in astable mode.

Light sensor:

Light measurement is done via VEML7700 IC.

Package:

Project is packaged in an IP67 plastic case.

-Pump:

The control element of the system is one 12V pump, a Barwig 0333.

-Power Supply:

The device is powered with an LPV-35-12 power supply unit, which provides 12V DC for the pump.
-Schematic:

-PCB layout:

-Prototype Hardware: